## Slide 1: Computed Tomography (CT) scan
Tarun(IMT2022034)
Tahir(IMT2022100)
Chaitanya(IMT2022545)
Karthikeyan(IMT2022569)

## Slide 2: Radiology
X-ray
CT Scan
MRI
Ultra Sound

## Slide 3: Basics Of X-Ray
X-ray Generation
When electrons strike the target:
  Bremsstrahlung radiation: continuous X-ray spectrum, due to deceleration of electrons in the Coulomb field of tungsten nuclei.
  Characteristic radiation: discrete peaks from electron shell transitions in tungsten atoms.
Result → Polychromatic X-ray beam, later filtered to remove very low-energy photons (which would add dose without contributing to image quality).

## Slide 4: Basics Of X-Ray
X-ray Interactions with Matter
When X-rays pass through tissue, photons are either absorbed, scattered, or transmitted.
  Photoelectric Effect
  Compton Scattering
  Coherent (Rayleigh) Scattering
Attenuation Law
I0 = Incident Intensity
µ = linear attenuation coefficient
X = thickness of material
I = I0e-µx

## Slide 5: Disadvantage Of X-Ray
Superposition of Structures

## Slide 6: Introduction to CT Scan
CT scan combines X-rays and computer-based reconstruction to generate cross-sectional images of the body.
Using mathematical reconstruction, CT produces a 3D map of tissue attenuation coefficients.
CT provides high-resolution anatomical detail, excellent soft tissue contrast, and the ability to reconstruct images in multiple planes or 3D volumes.

## Slide 7
X-ray vs CT Scan

## Slide 8: CT challenge?

## Slide 9: Radon Transform
f(x,y) → the 2D object(image function)
L → a line at angle θ and distance ρ from the origin,
ds → infinitesimal element along the line,
R{f} → Radon transform operator.

## Slide 10: Radon transform
R(θ,s) is an integral transform.
Its inverse is not a simple algebraic operation (like a matrix inverse) but involves solving an integral equation.
Writing down and computing the inverse Radon directly is messy, numerically unstable, and not practical for large images.

## Slide 11: Fourier Slice Theorem and Use of it in CT Scan
The 1D Fourier transform of the projection at angle θ\thetaθ is exactly the 2D Fourier transform of the image f(x,y)f(x,y)f(x,y) along a radial line in frequency space.
So, by collecting many projections at many angles, you can fill out the 2D Fourier space of the image.

## Slide 12: Units Used in CT Scan

## Slide 13: Reconstuction of Images in CT Scan

## Slide 14: Thank You